## Slide 1: Error Detection and Correction
Dr. Nitin Rakesh

## Slide 2: How Hamming Codes Work
One parity bit can tell us an error occurred
Multiple parity bits can also tell us where it occurred
O(lg(n)) bits needed to detect and correct one bit errors

## Slide 3: Hamming (7, 4)
7 bits total
  4 data bits
  3 parity bits
Can find and correct 1 bit errors
  or
Can find but not correct 2 bit errors

## Slide 4: Hamming Bits Table

## Slide 5: Example
Byte 1011 0001 Two data blocks, 1011 and 0001. Expand the first block to 7 bits: _ _ 1 _ 0 1 1. Bit 1 is 0, because b3+b5+b7 is even. Bit 2 is 1, b3+b6+b7 is odd. bit 4 is 0, because b5+b6+b7 is even. Our 7 bit block is: 0 1 1 0 0 1 1
Repeat for right block giving 1 1 0 1 0 0 1
0 0 0 1

## Slide 6: Example
Byte 1011 0001 Two data blocks, 1011 and 0001. Expand the first block to 7 bits: _ _ 1 _ 0 1 1. Bit 1 is 0, because b3+b5+b7 is even. Bit 2 is 1, b3+b6+b7 is odd. bit 4 is 0, because b5+b6+b7 is even. Our 7 bit block is: 0 1 1 0 0 1 1
Repeat for right block giving 1 1 0 1 0 0 1

## Slide 7: Example
Find Hamming bit for
i) 11011001
ii) 00010100
iii) 11111111
iv) 01011010

## Slide 8: Hamming Code Syndrome Design Criteria

## Slide 9: A Layout of Data and Check Bits that Achieves Our Design Criteria:
C1 is a parity check on every data bit whose position is xxx1
C1 = D1 exor D2 exor D4 exor D5 exor D7
C2 is a parity check on every data bit whose position is xx1x
C2 = D1 exor D3 exor D4 exor D6 exor D7
C4 is a parity check on every data bit whose position is x1xx
C4 = D2 exor D3 exor D4 exor D8
C8 is a parity check on every data bit whose position is 1xxx
C8 = D5 exor D6 exor D7 exor D8
Why this ordering? Because we want the syndrome, the Hamming test word, to yield the address of the error.

## Slide 10: Example:
Data stored = 00111001
Check bits:
Putting it together:

## Slide 11: Example:
Data stored = 00111001
Check bits:
Putting it together:

## Slide 12: Example:
Data stored = 00111001
Check bits:
Putting it together:

## Slide 13: Example:
Data stored = 00111001
Check bits:
Putting it together:

## Slide 14: Example:

## Slide 15: Example:
Word fetched:
Check Bits:
Putting it all together:
Comparing:
C8 C4 C2 C1
0 1 1 1 Orig Check Bits
0 0 0 1 New Check Bits
0 1 1 0 Syndrome
0110 = 6  bit position 6 is wrong, i.e. bit D3 is wrong

## Slide 16: Increased word length for error correcting

## Slide 17
Hamming Code: Example
7-bit
. Hamming codes can only correct single errors.
. But, to correct bursts of errors, send column by column.

## Slide 18
Hamming Code: Example
7-bit
. Hamming codes can only correct single errors.
. But, to correct bursts of errors, send column by column.

## Slide 19: Cyclic Redundancy Check (CRC)
Mostly used in data communication
Tells us whether an error has occurred, but does not correct the error.
This is a type of “systematic error detection”
  The error-checking bits are appended to the information byte

## Slide 20: Cyclic Redundancy Check (CRC)
Bit strings represented as polynomials with coef. 0 and 1.
K bit frame =>xk-1+…+1 (first and last coef must be 1)
Example
  110001 => x5+x4+1
Polynomial arithmetic is done module 2 i.e.  addition/subtraction = XOR operation

## Slide 21: Cyclic Redundancy Check (CRC)
Bit strings represented as polynomials with coef. 0 and 1.
K bit frame =>xk-1+…+1 (first and last coef must be 1)
Example
  110001 => x5+x4+1
Polynomial arithmetic is done module 2 i.e.  addition/subtraction = XOR operation

## Slide 22: CRC
Sender (S) and Receiver (R) agree on a generator polynomial G(x)
Frame – m bits => M(X) – the checksum of m is the remaining of R(x)=M(x)/G(x)
Checksum added to frame.
(R) Gets the frame M’(x)=[M(x)-R(x)]
  If M’(x)/G(x) has remainder => error

## Slide 23: Modulo 2 Arithmetic
Addition Rules
0 + 0 = 0 Ex: 1011
0 + 1 = 1 +110
1 + 0 = 1 1101
1 + 1 = 0

## Slide 24: Modulo 2 Arithmetic
Division
________
Ex: 1011 | 1001011
^ ^
divisor dividend

## Slide 25: Modulo 2 Arithmetic
Division
____1___
Ex: 1011 | 1001011
1011

## Slide 26: Modulo 2 Arithmetic
Division
____1___
Ex: 1011 | 1001011
1011
0010

## Slide 27: Modulo 2 Arithmetic
Division
____10__
Ex: 1011 | 1001011
1011
00100

## Slide 28: Modulo 2 Arithmetic
Division
____101_
Ex: 1011 | 1001011
1011
001001

## Slide 29: Modulo 2 Arithmetic
Division
____101_
Ex: 1011 | 1001011
1011
001001
1011

## Slide 30: Modulo 2 Arithmetic
Division
____101_
Ex: 1011 | 1001011
1011
001001
1011
0010

## Slide 31: Modulo 2 Arithmetic
Division
____1010
Ex: 1011 | 1001011
1011
001001
1011
00101

## Slide 32: Modulo 2 Arithmetic
Division
____1010  Quotient
Ex: 1011 | 1001011
1011
001001
1011
00101  Remainder

## Slide 33: Calculating and Using CRCs
Let the information byte F = 1001011
The sender and receiver agree on an arbitrary binary pattern P. Let P = 1011.
Shift F to the left by 1 less than the number of bits in P. Now, F = 1001011000.
Let F be the dividend and P be the divisor. Perform “modulo 2 division”.
After performing the division, we ignore the quotient. We got 100 for the remainder, which becomes the actual CRC checksum.
Add the remainder to F, giving the message M:
1001011 + 100 = 1001011100 = M

## Slide 34: Calculating and Using CRCs
M is decoded and checked by the message receiver using the reverse process.
____1010100
1011 | 1001011100
1011
001001
1001
0010
001011
1011
0000  Remainder

## Slide 35: CRC – Example, Transmitted Frame

## Slide 36: CRC - Example
Frame – 1101011011
G(x)=x4+x+1
Transmitted frame:
11010110110000 –
00000000001110
----------------------
11010110111110

## Slide 37: Reed-Solomon (RS)
Operates at block level instead of bit level
- RS(n, k) codes are defined using the following parameters
s = the number of bits in a char (8 bits)
k = the number of s-bit characters comprising the data block
n = the number of bits in the code word
RS(n, k) can correct (n – k)/2 errors in the k information bytes
EX: RS(255, 223)
can correct up to 16 erroneous bytes in the information block

## Slide 38: Summary
3 Types of Error Detection/Correction Methods
  Cyclic Redundancy Check (CRC)
    Used primarily in communication
    Can only detect errors.
  Hamming Codes
    Can detect and correct errors.
    The more parity bits added, the more errors can be detected and corrected.
    Used to detect errors in memory bits or fixed magnetic disk drives, in which errors occur randomly.

## Slide 39: Summary
  Reed-Solomon (RS)
    Can detect errors that occur in blocks (adjacent errors)
    Used to detect errors in removable media such as magnetic tapes or compact disks, in which “burst errors” occur due to mishandling and environmental stress.
Ch 2.7 > Summary

## Slide 40: Flow + Error Control
How do Layer 2 protocols implement them?
What’s a frame?
F
F
H
T
Payload
. What’s F?
. What’s in T?
. What’s in H?

## Slide 41: Header and Trailer
Trailer typically has checksum.
  How is it used/processed?
Header has: type, sequence number, and ack.

## Slide 42: Stop-and-Wait
Simplest form of flow control.
How does it work? (assume error-free channel)
  (1) Send 1 frame;
  (2) Wait for ACK.
  (3) Go to 1.

## Slide 43: Stop-and-Wait: Pros and Cons
Very simple!
But, poor link utilization.
  High data rates.
  Long propagation delay.

## Slide 44: Noisy Channels

## Slide 45: Stop-and-Wait in Noisy Channels
Need timers, retransmissions, and duplicate detection.
Use sequence numbers.
  Why?
  Distinguish frames.
  How large (e.g., in number of bits) are sequence numbers?

## Slide 46: ARQ Protocols
Automatic Repeat reQuest.
  Protocols that wait for ACK before sending more data.
ACKs now are used for flow AND error control.
What can happen?
  At receiver: frame arrives correctly, frame arrives damaged, or frame does not arrive.
  At sender: ACK arrives correctly, ACK arrives damaged, or ACK does not arrive.

## Slide 47: ARQ Protocols
Sender:
  Send frame 0.
  Start timer.
  If ACK 0, arrives, send frame 1.
  If timeout, re-send frame 0.
Receiver:
  **Waits for frame.
  If frame arrives, check if correct sequence number.
  Then send ACK for that frame.
  Go to (**)

## Slide 48: Simplex versus Duplex Transmission
Simplex:
  Send data in one channel and control in another channel.
Duplex:
  Send data and control on the same chanel.

## Slide 49: Can we do better?
Can we do better?
  Piggybacking.
  Bi-directional transmission.
  Wait for data packet and use that to piggyback the ACK.
  Use ACK field: only a few additional bits in the header.
But, how long should Layer 2 wait to send an ACK?
  ACK timers!

## Slide 50: Sliding Window Protocols
Window: number of “outstanding” frames at any given point in time.
  So what’s the window size of Stop and Wait?
Every ACK received, window slides.

## Slide 51
Sliding Window: Example
A sliding window of size 1, with a 3-bit sequence number.(a) Initially; (b) After the first frame has been sent; (c) After the first frame has been received;(d) After the first acknowledgement has been received.

## Slide 52: Sliding Window: Basics
Allows multiple frames to be in transit at the same time.
Receiver allocates buffer space for n frames.
Transmitter is allowed to send n (window size) frames without receiving ACK.
Frame sequence number: labels frames.

## Slide 53: Sliding Window: Receiver
Receiver ack’s frame by including sequence number of next expected frame.
  Cumulative ACK: ack’s multiple frames.
Example: if receiver receives frames 2,3, and 4, it sends an ACK with sequence number 5, which ack’s receipt of 2, 3, and 4.

## Slide 54: More Sliding Window …
Sender maintains sequence numbers it’s allowed to send; receiver maintains sequence number it can receive.
Sequence numbers are bounded; if frame reserves k-bit field for sequence numbers, then they can range from 0 … 2k -1k.
Transmission window shrinks each time frame is sent, and grows each time an ACK is received.

## Slide 55
Example: 3-bit sequence number and window size 7
0
1
2
0 1 2 3 4 5 6 7 0 1 2 3 4
0 1 2 3 4 5 6 7 0 1 2 3 4
ACK 3
0 1 2 3 4 5 6 7 0 1 2 3 4
3
4
5
6
ACK 4
0 1 2 3 4 5 6 7 0 1 2 3 4
0 1 2 3 4 5 6 7 0 1 2 3 4
0 1 2 3 4 5 6 7 0 1 2 3 4
0 1 2 3 4 5 6 7 0 1 2 3 4
0 1 2 3 4 5 6 7 0 1 2 3 4
A (Sender) B (Receiver)
0 1 2 3 4 5 6 7 0 1 2 3 4… 0 1 2 3 4 5 6 7 0 1 2 3 4

## Slide 56
One-Bit Sliding Window Protocol
Two scenarios: (a) Normal case. (b) Abnormal case. Notation is (seq, ack, packet number). An * indicates where a network layer accepts packet. ACK indicates last sequence number received.

## Slide 57: Bandwidth-Delay Product
How large should the sender’s window be?
Function of how “fat” is the pipe?
S
R
RTT
BW
W = BW*RTT/data size

## Slide 58: Pipelining
Pipelining and error recovery. Effect on error when (a) Receiver’s window size is 1. (b) Receiver’s window size is large.
Receiver’s
window size
is 1: discard
frames after error
with no ACK.
Receiver’s
window size
is large: buffers
all frames until error
recovered.
Selective Repeat
Go Back N