## Slide 1: Basic Electronics Engineering
3CSE3 & 3CSE4
No. of modules : 5
Sessions Planned: 68
Credit: 4
No of students registered: 63 (3CSE3)

## Slide 2: Module 1: Semiconductor Diodes & Diode Circuits
13 Hr lectures + 6 Hr Lab

## Slide 3: Prerequisites
To understand this presentation, you should have the following prior knowledge:
  Draw the structure of an atom, including electrons, protons, and neutrons.
  Define resistance and conductance.
  Label an electronic schematic, indicating current flow.
  Define Ohm’s and Kirchhoff’s laws.
  Describe the characteristics of DC and AC (sine wave) voltages.

## Slide 4: Student Learning Outcomes
Upon completion of viewing this presentation, you should be able to:
  Define conductor, insulator and semiconductor, and state the resistance or conductance of each.
  Name the current carriers in N and P-type material.
  Analyze the characteristics of PN junction diode and zener diode.
  Application of diodes as clippers and clampers.

## Slide 5: Semiconductor Material: Ge, Si and GaAs
Semiconductor Material type
Single Crystal eg. Si and Ge
Compound eg. GaAs, CdS, GaN and GaAsP
Most used

## Slide 6: Si and Ge atomic structure
Si atomic no is 14 (2,8,4)
Ge atomic no is 32 (2,8,18,4)

## Slide 7: GaAs

## Slide 8: Covalent bonding of Si and GaAs
Si has four valence electrons.
Therefore, it can form covalent bonds with
four of its neighbors.
When temperature goes up,
electrons in the covalent bond can
become free.

## Slide 9: Electron-hole pair interaction
With free electrons breaking off covalent bonds, holes are generated.
Holes can be filled by absorbing other free electrons, so effectively there is a flow of charge carriers.

## Slide 10: Covalent bonding of GaAs
Ga has valancy of 3
As has valancy of 5

## Slide 11: Intrinsic carriers (300K)
Semiconductor | Intrinsic Carriers ( per cubic cm)
GaAs | 1.7 x 10^6
Si | 1.5 x 10^10
Ge | 2.5 x 10^13
Intrinsic : very low impurity Semiconductor - As pure as can be possible.
Free electrons in a material due only to external causes are referred as intrinsic carriers.
Relative Mobility | 
Semiconductor | Mobility (cm^2/V.s)
Si | 1500
Ge | 3900
GaAs | 8500

## Slide 12: Temperature effect on SM:
Semiconductors have negative temperature coefficient ( conductivity increases with application of heat)
Conductors have positive temperature coefficient ( conductivity decreases with application of heat)

## Slide 13: Different Types of Solids
Fermi level falls between bands, with a large band gap. SiO2: 9 eV.
>5eV
Fermi level falls between bands, with a small band gap.Si: 1.11 eV, Ge:0.67 eV, GaAs: 1.43
Fermi level falls inside the energy band. Easy for electrons to move around
Fermi level

## Slide 14: Extrinsic Materials: N- type
Pure Si can be doped with other elements to change its electrical properties.
For example, if Si is doped with P (phosphorous), then it has more electrons, or becomes type N (electron).
Diffused impurities with 5 valence electrons are called donor atoms eg. Antimony, arsenic , phosphorous.
Free Electron

## Slide 15
At room temperature in an intrinsic Si, there is 1 free electron for every 10^12 atoms.
If dosage level is 1 in 10 million (10^7), the ratio 10^12/ 10^7 = 10^5 indicates that the carrier concentration has increased by ratio of 100000:1

## Slide 16: P-type semiconductor
If Si is doped with B (boron), then it has more holes, or becomes type P.
Boron, gallium, indium can be used.
The diffused impurity with 3 valance electrons are called acceptor atoms.

## Slide 17: Summary of charge carriers

## Slide 18: Electron-Hole density
Majority Carriers :
Minority Carriers :
Majority Carriers :
Minority Carriers :
The product of electron and hole densities is ALWAYS equal to the square of intrinsic electron density regardless of doping levels.

## Slide 19: Electron versus hole flow
The valence electron acquires sufficient kinetic energy to break its covalent bond and fills the void created by hole
When the electron move to fill the hole therefore a transfer of holes to the left and electrons to the right
This flow is known as conventional flow.

## Slide 20: Majority and Minority Carriers
N-type material, the electron is called majority carrier and hole the minority carrier
P-type material, the hole is called majority carrier and electron the minority carrier.

## Slide 21: Semiconductor Diode
Fig.
1
.
9
Boron impurity in p
-
type material.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
10
Electron versus hole flow.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
11
(a) n
-
type material; (b) p
-
type material.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
12
A p
–
n junction with no external bias. (a) An internal distribution of charge; (b) a diode symbol, with the
defined polarity and the current direction; (c) demonstration that the net carrier flow is zero at the external terminal of
the device when
V
D
=
0
V
.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
13
Reverse
-
biased p
–
n junction. (a) Internal distribution of charge under reverse
-
bias conditions; (b) reverse
-
bias polarity and direction of reverse saturation current.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
14
Forward
-
biased p
–
n junction. (a) Internal distribution of charge under forward
-
bias conditions; (b) forward
-
bias polarity and direction of resulting current.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
15
Silicon semiconductor diode characteristics.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
16
Plot of
e
x
.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
17
Zener region.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
18
Comparison of Ge, Si, and GaAs diodes.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
9
Boron impurity in p
-
type material.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
10
Electron versus hole flow.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
11
(a) n
-
type material; (b) p
-
type material.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
12
A p
–
n junction with no external bias. (a) An internal distribution of charge; (b) a diode symbol, with the
defined polarity and the current direction; (c) demonstration that the net carrier flow is zero at the external terminal of
the device when
V
D
=
0
V
.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
13
Reverse
-
biased p
–
n junction. (a) Internal distribution of charge under reverse
-
bias conditions; (b) reverse
-
bias polarity and direction of reverse saturation current.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
14
Forward
-
biased p
–
n junction. (a) Internal distribution of charge under forward
-
bias conditions; (b) forward
-
bias polarity and direction of resulting current.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
15
Silicon semiconductor diode characteristics.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
16
Plot of
e
x
.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
17
Zener region.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
18
Comparison of Ge, Si, and GaAs diodes.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
9
Boron impurity in p
-
type material.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
10
Electron versus hole flow.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
11
(a) n
-
type material; (b) p
-
type material.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
12
A p
–
n junction with no external bias. (a) An internal distribution of charge; (b) a diode symbol, with the
defined polarity and the current direction; (c) demonstration that the net carrier flow is zero at the external terminal of
the device when
V
D
=
0
V
.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
13
Reverse
-
biased p
–
n junction. (a) Internal distribution of charge under reverse
-
bias conditions; (b) reverse
-
bias polarity and direction of reverse saturation current.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
14
Forward
-
biased p
–
n junction. (a) Internal distribution of charge under forward
-
bias conditions; (b) forward
-
bias polarity and direction of resulting current.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
15
Silicon semiconductor diode characteristics.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
16
Plot of
e
x
.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
17
Zener region.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.
Fig.
1
.
18
Comparison of Ge, Si, and GaAs diodes.
Robert L. Boylestad
Electronic Devices and Circuit Theory,
9
e
Copyright ©
2006
by Pearson Education, Inc.
Upper Saddle River, New Jersey
07458
All rights reserved.

## Slide 29: Shockley’s Equation
Reverse Saturation current
Thermal voltage
K is Boltzmann’s Constant =
T = absolute temperature in kelvin
Q = charge of electron (
Applied Forward Bias Voltage

## Slide 30: ???
The arrow direction in the diode symbol indicates
a. Direction of electron flow.
b. Direction of hole flow (Direction of conventional current)
c. Opposite to the direction of hole flow
d. None of the above
Ans : B

## Slide 31
When the diode is forward biased, it is equivalent to
a. An off switch
b. An On switch
c. A high resistance
d. None of the above
Ans : B

## Slide 32: ???
At temperature of determine the thermal voltage
Ans: 25.875 mV

## Slide 33
Under normal reverse bias voltage applied to diode, the reverse current in Si diode
a. 100 mA
b. order of μA
c. 1000 μA
d. None of these
Ans: B

## Slide 35: Knee voltage…

## Slide 40
In the reverse bias region the reverse saturation current of a silicon diode doubles for every 10 degee C rise in temperature.

## Slide 45: ???
Determine the DC resistance levels for diode at
Diode current= 2mA and 20mA
Diode voltage= 10V

## Slide 46: Ans

## Slide 47: ???

## Slide 48: Ans

## Slide 49: Ans

## Slide 52: Simplified equivalent circuit

## Slide 53: Ideal Equivalent circuit

## Slide 56
Storage Time & Transition Time

## Slide 59: Zener Characteristics

## Slide 60
Zener effect and Zener diode
  When a Zener diode is reverse-biased, it acts at the breakdown region, when it is forward biased, it acts like a normal PN junction diode
Avalanche Effect
  Gain kinetic energy – hit another atom –produce electron and hole pair

## Slide 61
Voltage Regulator using Zener Diode
1. The zener diode holds the voltage constant regardless of the current
2. The load resistor sees a constant voltage regardless of the current
The remainder of VPS drops across Ri

## Slide 62
Zener Diode as Voltage Regulator
Three Cases:
Fixed
Fixed
Fixed .
Case 1: Determine the state of zener diode by removing it from the network and calculating the voltage across the resulting open circuit.

## Slide 63
If V > Vz zener diode is on, the the appropriate equivalent model can be substituted.
If V < Vz zener diode is off, the open circuit model can be substituted
2. If zener diode is ON

## Slide 64
Question:

## Slide 68
Case 2:
For fixed value of load resistance the input voltage must be sufficiently large to turn the zener diode on.
The mini. Turn on voltage is is determined by
And

## Slide 74
Case 3: Fixed load resistance and variable input supply

## Slide 78: LED…….What is an LED?
Light-emitting diode
Semiconductor
Has polarity

## Slide 79: Inside a Light Emitting Diode
Transparent Plastic Case
Terminal Pins
Diode
Wavelength

## Slide 80: LED: How It Works
When current flows across a diode
Negative electrons move one way and positive holes move the other way

## Slide 81: LED: How It Works
The holes exist at a lower energy level than the free electrons
Therefore when a free electrons falls it losses energy

## Slide 82: LED: How It Works
This energy is emitted in a form of a photon, which causes light
The color of the light is determined by the fall of the electron and hence energy level of the photon

## Slide 83: Kinds of LEDs

## Slide 84: How to Connect a LED:
Requires 1.5~2.5V and 10 mA
To prevent overloading, use resistor 470 Ω

## Slide 85: How to Connect a LED:

## Slide 86: Connect LED to BS2
LED is on when P0 is high
LED is on when P1 is low

## Slide 87: Connect Multiple LEDs to BS2
8 LEDs are connected to BS2 each I/O pin (P0-P7) is allowed to sink 6.25mA

## Slide 88: Case Study: Blinking LED

## Slide 89: Case Study: Blinking LED
Pbasic program to make an LED blink
output 0
Main:
low 0
pause 1000
high 0
pause 1000
goto Main
Make pin0 an output
Loop begins here
Turn LED on
Pause for 1 sec
Turn LED off
Pause for 1 sec
Go back to beginning of loop

## Slide 90: Experiments
Flash an LED
    Single LED
    Multiple LEDs
Traffic Light by use of LEDs

## Slide 91: Diode as a Rectifier
Half wave rectifier
Full wave Rectifier- center Tap & Bridge Rectifier

## Slide 92: Single-Phase Half-Wave Rectifier

## Slide 93: Waveforms

## Slide 94: Single-Phase Half-Wave Rectifier

## Slide 95: Performance Parameters
Average value of the output voltage, Vdc
Average value of the output current, Idc
Output dc power, Pdc
  Pdc = VdcIdc
rms value of the output voltage, Vrms
Output ac power, Pac
  Pac = VrmsIrms

## Slide 96: Performance Parameters (continued)
Efficiency, η
  η = Pdc/Pac
Effective (rms) value of the ac component of the output voltage, Vac
  Vac = Vrms2 – Vdc2
Form factor, FF
  FF = Vrms/Vdc
Ripple factor, RF
  RF = Vac/Vdc

## Slide 97: Performance Parameters (continued)
Alternate form for ripple factor
Transformer utilization factor, TUF
  TUF = Pdc/VsIs
  Vs, Is are rms voltage and current of the transformer secondary

## Slide 98: Input Voltage and Current

## Slide 99: Performance Parameters (continued)
Displacement angle, Φ
Displacement Factor, DF
  DF = cos(Φ)
Harmonic Factor, HF

## Slide 100: Performance Parameters (continued)
Power Factor, PF

## Slide 101: Performance Parameters (continued)
Crest Factor, CF

## Slide 102: Example 3.1
Determine η, FF, RF, TUF, PIV of the diode, CF of the input current, input PF.

## Slide 103: Determine the Average Voltage, Vdc

## Slide 105: Determine the rms Voltage, Vrms

## Slide 106: Determine Pdc, Pac, and η

## Slide 107: Determine FF and RF

## Slide 108: Determine the TUF

## Slide 109: Determine the PIV
PIV is the maximum (peak) voltage that appears across the diode when reverse biased. Here, PIV = Vm.
-
+
+
-
PIV

## Slide 110: Determine CF

## Slide 111: Determine PF

## Slide 112: Summary – Half-Wave Rectifier
RF=121% High
Efficiency = 40.5 Low
TUF = 0.286 Low
  1/TUF = 3.496
  transformer must be 3.496 times larger than when using a pure ac voltage source

## Slide 113: Half-Wave Rectifier with R-L Load

## Slide 114: Waveforms of Current and Voltage
Conduction period of D1 extends beyond ωt = π

## Slide 115: Average Output Voltage
Increase average voltage and current by making σ = 0

## Slide 116: Waveforms with Dm installed

## Slide 117: Application as a Battery Charger
Diode conducts for vs > E, starting when Vmsinα = E

## Slide 118: Waveforms for the Battery Charger
Diode turns off when vs < E (at β = π – α)
Charging current io = (vs – E)/R
io = (Vmsinωt – E)/R for α < ωt < β

## Slide 119: FULL WAVE RECTIFIER
Center-Tapped
Bridge

## Slide 120: Single-Phase Full-Wave Rectifier
Center-Tapped Transformer

## Slide 121: Waveforms for the Full-Wave Rectifier

## Slide 122: Single-Phase Full-Wave Rectifier
PIV = 2Vm

## Slide 123: Full-Wave Bridge Rectifier

## Slide 124: Waveforms for the Full-Wave Bridge

## Slide 125: Full-Wave Bridge with Waveforms
Conduction pattern
D1 – D2 D3 – D4
PIV = Vm

## Slide 126
Positive cycle, D2 off, D1 conducts;
Vo – Vs + V = 0
Vo = Vs - V
Full-Wave Rectification – circuit with center-tapped transformer
Since a rectified output voltage occurs during both positive and negative cycles of the input signal, this circuit is called a full-wave rectifier.
Also notice that the polarity of the output voltage for both cycles is the same
Negative cycle, D1 off, D2 conducts;
Vo – Vs + V = 0
Vo = Vs - V

## Slide 127
Vs = Vpsin t
V
-V
Notice again that the peak voltage of Vo is lower since Vo = Vs - V
Vp
Vs < V, diode off, open circuit, no current flow,Vo = 0V

## Slide 128
Positive cycle, D1 and D2 conducts, D3 and D4 off;
+ V + Vo + V – Vs = 0
Vo = Vs - 2V
Full-Wave Rectification –Bridge Rectifier
Negative cycle, D3 and D4 conducts, D1 and D2 off
+ V + Vo + V – Vs = 0
Vo = Vs - 2V
Also notice that the polarity of the output voltage for both cycles is the same

## Slide 129
A full-wave center-tapped rectifier circuit is shown in Fig. 3.1. Assume that for each diode, the cut-in voltage, V = 0.6V and the diode forward resistance, rf is 15. The load resistor, R = 95 . Determine:
  peak output voltage, Vo across the load, R
  Sketch the output voltage, Vo and label its peak value.
( sine wave )

## Slide 130
SOLUTION
peak output voltage, Vo
Vs (peak) = 125 / 25 = 5V
V +ID(15) + ID (95) - Vs(peak) = 0 ID = (5 – 0.6) / 110 = 0.04 A Vo (peak) = 95 x 0.04 = 3.8V
3.8V
Vo
t

## Slide 131
Duty Cycle: The fraction of the wave cycle over which the diode is conducting.

## Slide 132
EXAMPLE 3.1 – Half Wave Rectifier
Determine the currents and voltages of the half-wave rectifier circuit. Consider the half-wave rectifier circuit shown in Figure.
Assume and . Also assume that
Determine the peak diode current, maximum reverse-bias diode voltage, the fraction of the wave cycle over which the diode is conducting.
A simple half-wave battery charger circuit
-VR + VB + 18.6 = 0
VR = 24.6 V
- VR +
+
-

## Slide 134
The peak inverse voltage (PIV) of the diode is the peak value of the voltage that a diode can withstand when it is reversed biased

## Slide 135
Type of Rectifier | PIV
Half Wave | Peak value of the input secondary voltage, Vs (peak)
Full Wave : Center-Tapped | 2Vs(peak) - V
Full Wave: Bridge | Vs(peak)- V

## Slide 136: Example: Half Wave Rectifier
Given a half wave rectifier with input primary voltage, Vp = 80 sin t and the transformer turns ratio, N1/N2 = 6. If the diode is ideal diode, (V = 0V), determine the value of the peak inverse voltage.
Get the input of the secondary voltage:
80 / 6 = 13.33 V
PIV for half-wave = Peak value of the input voltage = 13.33 V

## Slide 137
EXAMPLE 3.2
Calculate the transformer turns ratio and the PIV voltages for each type of the full wave rectifier
center-tapped
bridge
Assume the input voltage of the transformer is 220 V (rms), 50 Hz from ac main line source. The desired peak output voltage is 9 volt; also assume diodes cut-in voltage = 0.6 V.

## Slide 138
Solution: For the centre-tapped transformer circuit the peak voltage of the transformer secondary is required
The peak output voltage = 9V
Output voltage, Vo = Vs - V
Hence, Vs = 9 + 0.6 = 9.6V
Peak value = Vrms x 2
So, Vs (rms) = 9.6 / 2 = 6.79 V
The turns ratio of the primary to each secondary winding is
The PIV of each diode: 2Vs(peak) - V = 2(9.6) - 0.6 = 19.6 - 0.6 = 18.6 V

## Slide 139
Solution: For the bridge transformer circuit the peak voltage of the transformer secondary is required
The peak output voltage = 9V
Output voltage, Vo = Vs - 2V
Hence, Vs = 9 + 1.2 = 10.2 V
Peak value = Vrms x 2
So, Vs (rms) = 10.2 / 2 = 7.21 V
The turns ratio of the primary to each secondary winding is
The PIV of each diode: Vs(peak)- V = 10.2 - 0.6 = 9.6 V

## Slide 140: Clipper and Clamper Circuits

## Slide 141: Clippers
Clipping circuit: A wave shaping circuit which controls the shape of the output waveform by removing or clipping a portion of the applied wave.
Half wave rectifier is the simplest example. (It clips negative half cycle).
Also referred as voltage limiters/ amplitude selectors/ slicers.
Applications:
- In radio receivers for communication circuits.
- In radars, digital computers and other electronic systems.
- Generation for different waveforms such as trapezoidal, or square
waves.
- Helps in processing the picture signals in television transmitters.
- In television receivers for separating the synchronising signals from composite picture signals

## Slide 142: Types of clippers
According to non- linear devices used:
- Diode clippers and Transistor clippers
According to biasing
- Biased clippers and Unbiased clippers.
According to level of clipping
- Positive clippers, Negative clippers and combination clippers

## Slide 143: THUMB RULE
Action of biasing on diode
When diode is forward biased, it acts as a closed switch ( ON state).
When diode is reverse biased, it acts as a open switch ( OFF state).

## Slide 144: Negative Series clipper

## Slide 145: Positive shunt clipper

## Slide 146: Biased Shunt Clippers

## Slide 147: Negative Shunt Biased clipper with Reverse polarity

## Slide 148: Positive Shunt Biased clipper with Reverse polarity

## Slide 150: Combinational Clipper

## Slide 151: Clampers
Add DC level to a waveform
Network must have capacitor, diode, and resistive element.

## Slide 152: Positive half cycle
For Positive half Cycle:
Diode acts like short circuit.
Capacitor charges up to V volts
During this interval the output is zero.

## Slide 153: Negative Half cycle
Diode acts like an open circuit.
The leakage time of C is very high (5T), hence it doesn’t leak quickly.
The total swing of the output is equal to the total swing of the input signal.

## Slide 154: Question
Determine the output voltage for the circuit:

## Slide 155
The analysis will begin with the period t1 → t2
Applying Kirchhoff’s voltage law around the input loop will result in
And output voltage is equal to 5 volts.

## Slide 156: For Next cycle
From t2  t3.

## Slide 157: Question 2
Repeat the above question with practical silicon diode with knee voltage of 0.7V

## Slide 159: Summary

## Slide 160: Clampers

## Slide 161
LOAD LINE AND Q-POINT
Analysis of a basic diode circuit
The applied load will normally have an impact on the region (or point) of operation of a device. If the analysis is performed in a graphical manner, a line can be drawn on the characteristics of the device to represent the applied load.
The intersection of the load line with the characteristics will determine the point of operation of the system. Physically, this point of operation mainly determines the conditions under which the device is to be operated in a circuit.
This case takes care of the various intriguing attributes of the circuit. This kind of an analysis is known as the load-line analysis.

## Slide 162
Under normal conditions, this resistance is approximately 10 Ω. Applying Kirchoff’s voltage law (KVL) of circuit theory, to the series, we obtain:
LOAD LINE AND Q-POINT
If VD = 0 V, we can calculate ID and plot the magnitude of ID on the vertical axis.
I-V characteristics of the diode
If ID = 0 A, we can calculate VD and plot the magnitude of VD on the horizontal axis.

## Slide 163
LOAD LINE AND Q-POINT
Illustration of a load line when: (1) voltage is constant and resistance varies (2) voltage varies and the resistance is constant
The load line on the characteristics of the diode
A straight line drawn between two points will define the load line.
If the value of R is changed, the intersection on the vertical axis will change. This affects the slope of the load line, and gives a different point of intersection between the load line and the device characteristics.
The point of intersection between the device characteristics and the load line (VD0 , ID0 ) is called the point of operation or the quiescent point (Q-point) as defined by a dc network.

## Slide 164
LOAD LINE AND Q-POINT
Change of Q-point with changes in supply voltage and load
Load line